## Slide 1: Hydroclimatic risks and uncertainty in the global power sector
Matthew Gidden1, Edward Byers1, Peter Greve1, Taher Kahil1 Simon Parkinson1, Catherine Raptis2, Joeri Rogelj1, Yusuke Satoh1, Michelle van Vliet3,1, Yoshide Wada1, Volker Krey1, Simon Langan1, and Keywan Riahi1
1 International Institute for Applied Systems Analysis, Austria
2 ETH Zurich, Switzerland
3 Wagenigen University, Netherlands
ERE1.2 Energy and environmental system interactions – Policy and modelling
European Geosciences Union General Assembly 2017
24/04/2017

## Slide 2: Water and climate impacts impacts assessment framework
Hydrological models
5 GHMs
Daily timestep
0.5°x0.5°
Global mean temperature change scenarios
Climate models
5 GCMs
Downscaled & bias corr. to 0.5°x0.5
RCP8.5
Climate impacts
Air temperature
Temp change
Heatwaves
Hydrology
Low flows
Seasonality
Flood risk
Water temp
1.5°C
2.0°C
3.0°C
Hist
Global power plants dataset + simulation models
Capacity subsets
Steam thermal
Non-steam thermal
Hydro & pumped storage
Risk identification matrix
Capacity subsets
Spatial units
Climate impact
Uncertainty analysis:
GCM & GHM agreement
Climate response
Power plant characteristics

## Slide 3: ISI-MIP – Inter-sectoral inter-comparison modelling project
Climate
Multi-model… multi-model… ensembles
Downscaled, bias-corrected climate model data
5 GCMs [HadGEM, IPSL, GFDL, NorESM, MIROC]
From ~2.5°x ~2.5° to 0.5°x0.5° grid
Historical + 4 RCPs, 1960-2100
Hydrology
Gridded hydrological models using bias-corrected GCM input forcings
Daily timestep data for runoff, evap, discharge, irrigation demands etc
Examples include:
  H.08 (U. Tokyo)
  PCR-GLOBWB (Utrecht)
  VIC (Washington State, Wagenigen)
  J.ULES (Met Office, CEH)
  WaterGAP (Frankfurt, Kassel, Potsdam)
  LPJmL (PIK)
  WBM (CUNY)
  MPI-HM (Max Planck Inst)
  Community Water Model (IIASA) – coming soon….

## Slide 4: Global power plant dataset
Platts WEPP – June 2013. Licensed database, with no lat/lon information
Carma – based on Platts WEPP ~2010, based on georeferencing algorithm by Kevin Ummel
Raptis – based on Platts WEPP March 2012 for thermal power plants
(Raptis et al. 2016)
Table 7. Top 10 basins (level 3) with capacity that need cooling water | 
Basin | MW
Mississippi Missouri | 257,386
Yangtze | 200,674
Gironde France West Coast | 175,940
Japan III | 154,181
Huang He | 132,464
China Coast | 118,941
Ziya He Interior | 111,299
North and South Korea Bo Hai Korean Bay North Coast | 108,105
Gulf of Mexico, North Atlantic coast | 104,056
China Coast 1 | 90,908
 | 1,453,955
Notes: 86% of global capacity with locations

## Slide 5: Indicators
Low flows and peak flows
Low flows
  Q90 (10th percentile)
Peak flows
  Flooding proxy
  Block-maxima approach
Variability
Seasonality
  Difference between wet & dry seasons
Inter-annual variability
  Variability of water availability between years

## Slide 6: Methodology: Low Flows
Powerplant database | 
Fuel types | [coal, bio, gas, hydro,…, sun]
Unit types | [CCGT, ST, CT,…IC, HY]
Cooling systems | [ot_fresh, cl_fresh,… air]
Status | [Operational, Planned, Retired]
Impact datasets | 
Hydrology | 
Q90 (low flows) | Statistical measure of low river flows
Peak flows | Indicator for flood impacts
Seasonality | Difference between wet & dry seasons
Inter-annual variability | Variability of annual water availability
Water temperature | 
Temperature change | 
Heat waves | Duration and frequency of hot days
Degree days | Measure of long term temperature change
+ water
- water

## Slide 7: Seasonality

## Slide 8: Multiple climate impact scoring
Negative climate impacts scored onto scales
Impacts scales can be adjusted according to preferences
Apply to multiple impacts to make a multi-impact hotspot map:
Q90 low flows
Seasonality
Inter-annual variability
Peak flows
Notes: Figures to be updated

## Slide 9: Impact Analysis

## Slide 10: Impact Analysis

## Slide 11: Robustness of climate impacts
Multi-model approaches allow exploration of model uncertainties
Information can be scored/weighted according to model uncertainty
High uncertainty doesn’t always mean poor information
Notes: If we have time we will do the Robustness test which is more comprehensive than looking at model agreement – and gives indication of where there are significant and robust changes.
Based on Knutti and Sedlacek 2012
http://www.nature.com/nclimate/journal/v3/n4/abs/nclimate1716.html
http://www.nature.com/nclimate/journal/v3/n4/extref/nclimate1716-s1.pdf

## Slide 12: Conclusions and Future Work
Large quantities of capacity affected
Largest combined impacts observed in China, US, and Russia
Not necessarily strict climate ordering
Take Aways
Model robustness (uncertainty) analysis
Aggregate indicator investigation
Disaggregating power plants
1.5 vs. 2-degrees
Up Next