## Slide 1: Global surface water reservoir storage under climate change, land use constraints, and population growth
Presenter: Lu Liu
Co-authors: Simon Parkinson, Matthew Gidden, Edward Byers, Yusuke Satoh, Keywan Riahi, and Barton Forman
Department of Civil and Environmental Engineering
University of Maryland
December 15th, 2016
San Francisco, CA
2016 AGU Fall Meeting

## Slide 2: Motivation
Reservoirs
Flood control
Hydro power
Irrigation
Water supply
Recreation
Relocation
Land occupation
Evaporation loss
GHG emissions
(321Tg out of 9500Tg, ~3.4%)
Three Gorges Dam Reservoir
Current global reservoir storage: 6197 km3 (source: GRanD)
Research questions:
What is the global exploitable reservoir storage capacity?
How does streamflow variations affect the reliability of potential reservoirs?
How will climate change, population growth and land-uses affect the potential storage?
Notes: Three Gorges Dam 22,500 MW 39.3 km3 (1045 km2)
Hoover Dam 2,000 MW 32.22 km3 (640 km2)
GRanD: Global Reservoir and Dam (GRanD) Database

## Slide 3: Methodology
Build Storage-Yield curves with Linear Programming
Modify Sequent Peak Algorithm (SPA) to incorporate evaporation loss from reservoirs
Firm Yield (water demand)
Storage-Yield curve
Notes: As such, percolation or seepage loss is small for most of the reservoirs and progressively gets lowered with the passage of time since the sediment getting deposited at the reservoir bottom helps to reduce percolation losses - See more at: http://rctechite.blogspot.co.at/2013/09/reservoir-losses-and-their-minimization.html#sthash.zrzM3QJV.dpuf

## Slide 4: Workflow
ISI-MIP
Storage-yield curves
GRanD reservoir data
Evaporation from reservoirs
Surface area-volume relationship
Global reservoir expansion potential and reliability
235 Global hydrological basins
Exclusion zones
(Population, irrigation areas, protected areas)
2020s
1971-2000
2030s
.
.
.
.
.
.
2080s
8 decadal runoff
Climate forcing from ISI-MIP
Notes: Proof of concept for methodology
Apply for full model combination
ISI-MIP: The Inter-Sectoral Impact Model Intercomparison Project

## Slide 5: Exclusion zones
Population
Irrigated land
Protected land
SSP
UNEP and IUCN
FAO
Unavailable land
Where reservoirs cannot take place

## Slide 6: Two examples of S-Y curves
Danube basin
California basin
Current
Exploitable
With E
No E
Notes: RCP2.6 (0.3 to 1.7)
RCP4.5 (1.1 to 2.6)
RCP6.0 (1.4 to 3.1)
RCP8.5 (2.6 to 4.8)

## Slide 7: Effect of net evaporation
Globally, net evaporation loss from reservoirs accounts for ~2-4% of the current annual firm yield (non-negligible)
Differences between basins are widened
Differences between RCPs are trivial
Increasing impact particularly under RCP8.5
RCP2.6
RCP4.5
RCP8.5
RCP6.0

## Slide 8: How much room for expansion?
Current global capacity ~6200km3
Without exclusion zones, potential capacity is ~5 times of current capacity
However, with exclusion zones, actual exploitable capacity is ~4 times of current capacity
Total firm yield ↑ by 40%

## Slide 9: Where are the marginal gains?
SSP1 2050s
Chart: Ganges-Brahmaputra Basin
| Current storage | Current yield | Exploitable storage | Exploitable yield
 | 44.15 | 476.7112 | 635.51 | 1063.5386
Low
High
Chart: Missouri River Basin
| Current storage | Current yield | Exploitable storage | Exploitable yield
 | 133.065 | 173.3488 | 140.39 | 173.6423
Existing
Exploitable
Existing
Exploitable

## Slide 10: Where to expand reservoirs?
SSP1 2050s
Low
High
Ganges-Brahmaputra Basin
Missouri River Basin

## Slide 11: Research outputs
  Data products
  Maps of reservoirs potential under different climate and socioeconomic pathways
  Reliability indicators for long-term reservoir planning
  Policy implications
  Identify regions where reservoir expansion will be particularly challenging
  Marginal gain by expanding reservoirs
  Is building reservoir the solution to water scarcity?

## Slide 12: Key messages
Environmental constraints and human development pose significant impact on exploitable reservoir storage (~7-15%)
Evaporation losses are non-trivial (~2-4%)
Regional disparity in reservoir reliability and potential for expansion
Provide scientific support for long-term planning of water infrastructure

## Slide 13: Acknowledgement
Young Scientists Summer Program (YSSP) at the International Institute for Systems Analysis (IIASA), Laxenburg, Austria
The Coupled Model Intercomparison Project Phase 5 (CMIP5) and the Inter-Sectoral Impact Model Intercomparison Project (ISI-MIP)

## Slide 14: Additional slides

## Slide 15
Climate | RCP2.6, RCP4.5, RCP6.0 and RCP8.5
Population | SSP1 and SSP3
Time periods | 1971-2000, 2020s, 2030s, 2040s, 2050s, 2060s, 2070s and 2080s
Model | PCR-GLOBWB (GHM) HadGEM2-ES (GCM)

## Slide 16: GRanD reservoir database
~6100km3

## Slide 17: 235 hydrological basins

## Slide 18: Area-volume relationship
Chart: Volume (MCM)
Surface area-volume relationship (log scale) derived from GRanD reservoir database (specific for each of the 235 basin)

## Slide 19: Effect of population growth and land-uses
Increasing impact on reservoir potential over time due to increasing total population
Higher urbanization, smaller impact on reservoir potential
More rural population relocation, smaller impact on reservoir potential
SSP1: high urbanization
SSP3: low urbanization
Reduction in potential storage

## Slide 20: Linear Programming
Find the minimum capacity that can fulfill the following subject functions.

## Slide 21: Sensitivity analysis on temporal resolution
No substantial differences

## Slide 22: Compute reliability
Run the analysis for multiple years and RCPs
Compute reliability indicator

## Slide 23
Net evaporation in mm/day in the 2080s under RCP8.5 scenario
Difference of net evaporation loss in the 2080s between RCP8.5 and RCP2.6

## Slide 24
Cumulative spatial distribution of change of net evaporation in the 2080s relative to historical period under RCP2.6 and RCP8.5.

## Slide 25: Future directions for this work
The ability to adapt
  Where are we currently on the curve?
  How much additional storage is there?
The need to adapt
  Is there water scarcity?
  How much does it cost?
Social potential to adapt
  Strength of government
  Economic-institutional capacity

## Slide 26: Possible improvements
Evaporation from reservoirs
  Should reflect excluded areas
Area-volume relationship
  More robustness
Exclusion zones
  Digital Elevation Model
  Decision criteria
Environmental flow
  Varies by season and geographic location