## Slide 1: Pathways towards clean air in India
Pallav Purohit IIASA Air Quality and Greenhouse Gases Program
EGU 2019 Vienna, April 11, 2019

## Slide 2: Fine particulate matter (PM2.5) concentration in Indian cities
Chart: PM2.5 concentration (annual average, µg/m3)
| Agra | Ahmedabad | Chandrapur | Delhi | Faridabad | Gaya | Gurgaon | Jaipur | Jodhpur | Kanpur | Kolkata | Lucknow | Mumbai | Muzaffarpur | Nagpur | Patiala | Patna | Varanasi
 | 131 | 65 | 60 | 143 | 172 | 149 | 120 | 105 | 98 | 173 | 74 | 138 | 64 | 120 | 84 | 101 | 144 | 146
NAAQS
WHO guideline
Source: WHO (2018)

## Slide 3: The study tools The GAINS (Greenhouse gas - Air Pollution INteractions and Synergies) and GCAM-IIMA models
National emission ceilings
Decision making on air quality management
Policy targets
Emissions
Emission control options: ~1000 measures, co-control of 10 air pollutants and 6 GHGs)
Atmospheric dispersion
Costs
Health, ecosystems and climate impact indicators
Optimization
GCAM/IIMA
Energy activity projections
Buildings
Industry
Transport

## Slide 4: Air quality management needs to address urban and rural areas
While current ambient PM2.5 monitoring in India reveals high levels in urban areas, remote sensing, comprehensive air quality modelling and emission inventories suggest large-scale exceedances of the NAAQS also in rural areas.
Household fuel combustion, small industries, burning of garbage and agricultural waste, etc., cause high emissions in rural areas too.
Pollution from rural areas is transported into the cities (and vice versa), where it constitutes a significant share of pollution.
Emission densities of PM2.5, 2015
Source: IIASA/GAINS
Computed ambient levels of PM2.5
Satellite-derived PM2.5
Source: NASA
Source: IIASA/GAINS
PM2.5 (kt/year)

## Slide 5: Effective solutions require regional cooperation between cities and States
A large share of PM2.5 in ambient air originates from sources outside of cities and from other States, which are beyond the immediate jurisdictions of cities.
(Cost-)effective strategies require regionally coordinated approaches, and need to address urban and rural emission sources.
Source: IIASA/GAINS
Origin of (population-weighted) PM2.5 concentrations in ambient air 2015

## Slide 6: Effective solutions must address all sources that contribute to PM2.5 formation
A significant share of emissions still originates from sources associated with poverty and underdevelopment (i.e. solid fuel use in households and waste management practices).
Any effective reduction of PM2.5 levels in ambient air and the resulting health burden needs to balance emission controls across all these source sectors.
A focus on single sources alone will not deliver effective improvements and is likely to waste economic resources to the detriment of further economic and social development.
*Secondary particles formed in the atmosphere from agricultural NH3 emissions through
chemical reactions with SO2 and/or NOx emissions; **Including Telangana
Source: IIASA/GAINS

## Slide 7: Macro-economic development and energy consumption
Source: CEEW/IIASA

## Slide 8: Compliance with current legislations will be essential for stabilizing pollution levels as the economy grows
2015
2030 with current legislations
Computed ambient levels of PM2.5
Source: IIASA/GAINS
Current emission controls are effective, but their impacts are compensated by rapid economic growth.
By 2030, effective implementation and enforcement of the 2018 legislation could allow a three-fold increase in GDP without further deteriorating air quality.

## Slide 9: Policies and measures are available that could bring air quality more in compliance with the NAAQS -Advanced Emission Control Technology Scenario
2015
2030 with current legislations
Computed ambient levels of PM2.5
Source: IIASA/GAINS
Advanced technical emission controls can deliver additional air quality improvements, but will not be sufficient to achieve the NAAQS everywhere
  NAAQS-compliant air quality to 60% of the Indian population
2030 with advanced controls

## Slide 10: Policies and measures are available that could bring air quality more in compliance with the NAAQS -Sustainable Development Scenario
2015
2030 with current legislations
Computed ambient levels of PM2.5
2030 with development measures
Source: IIASA/GAINS
A package of development measures that are usually taken for other policy priorities can deliver significant co-benefits on air quality.
  NAAQS-compliant air quality to about 85% of the Indian population.

## Slide 11: Air pollutant emission control costs
Air pollution emission control costs accounted for about 0.7% of the GDP in 2015. This share will increase to 1.4-1.7% of GDP in 2030. More than 80% of total costs emerged for mobile sources.
In 2050, with an almost 10-fold increase in GDP, air pollution controls will consume 1.1-1.5% of the GDP.
Source: IIASA/GAINS

## Slide 12: Sustainable development measures can deliver a wide range of benefits
In the sustainable development scenario, India’s CO2 emissions would be about 60% lower in 2050 than in the baseline case.
Even without dedicated measures focused on methane, CH4 emissions would be 40% lower in 2050 compared to the baseline case.
Black carbon emissions would decline by 80% in the development scenario in 2050 compared to 2015.
Source: IIASA/GAINS

## Slide 13: Priority measures
Access to clean fuels and technologies for cooking (e.g., promotion of LPG/electric stoves)
Effective implementation of current policy measures (e.g., FGD in power plants, BS-VI from 2020)
Improved waste management and agricultural production practices
Substituting coal with natural gas and renewables (solar/wind) in power generation and industry
Improvements in energy efficiency (power, industry, transport and residential/commercial)
Advanced emission controls (e.g., HED and ESP Stage-II for PM and SCR for NOx control in power plants)
Enhanced public transport (e.g., metro) and increased incentives for greater adoption of electric vehicles
Emission control on non-industrial sources (e.g., road dust)
Coordination of urban, rural and inter-State responses

## Slide 14: GAINS India: A productive CEEW-IIASA cooperation
  Markus Amann
  Jens Borken-Kleefeld
  Gregor Kiesewetter
  Adriana Gomez-Sanabria
  Zbigniew Klimont
  Pallav Purohit
  Peter Rafaj
  Robert Sander
  Wolfgang Schöpp
  Vaibhav Chaturvedi
  Hem H. Dholakia
  Poonam Nagar Koti

## Slide 15: The GAINS-South Asia tool is available online to explore cost-effective strategies that maximize multiple benefits Access on the Internet: http://gains.iiasa.ac.at Thank you! purohit@iiasa.ac.at