## Slide 1: Machine learning and meteorological data for spatio-temporal prediction of tropospheric parameters
Laura Crocetti - lcrocetti@ethz.ch, B. Soja, G. Kłopotek, M. Awadaljeed, M. Rothacher, L. See, R. Weinacker, T. Sturn, I. McCallum, V. Navarro
27th May 2022, EGU22

## Slide 2: Motivation
Global Navigation Satellite System (GNSS) – a suitable tool for studies on the atmosphere
Radio signals transmitted by GNSS propagate through the atmosphere – atmospheric parameters can be estimated
GNSS
atmosphere
Laura Crocetti – lcrocetti@ethz.ch

## Slide 3: Motivation
Global Navigation Satellite System (GNSS) – a suitable tool for studies on the atmosphere
Radio signals transmitted by GNSS propagate through the atmosphere – atmospheric parameters can be estimated
Make use of thousands of GNSS stations
  model tropospheric parameters based on meteorological data using Machine Learning (ML)
atmosphere
GNSS
Laura Crocetti – lcrocetti@ethz.ch

## Slide 4: Motivation
Global Navigation Satellite System (GNSS) – a suitable tool for studies on the atmosphere
Radio signals transmitted by GNSS propagate through the atmosphere – atmospheric parameters can be estimated
Make use of thousands of GNSS stations
  model tropospheric parameters based on meteorological data using Machine Learning (ML)
Latitude
Longitude
Zenith Wet Delay (ZWD)
Laura Crocetti – lcrocetti@ethz.ch

## Slide 5: Motivation
Global Navigation Satellite System (GNSS) – a suitable tool for studies on the atmosphere
Radio signals transmitted by GNSS propagate through the atmosphere – atmospheric parameters can be estimated
Make use of thousands of GNSS stations
  model tropospheric parameters based on meteorological data using Machine Learning (ML)
Latitude
Longitude
Time
Zenith Wet Delay (ZWD)
Laura Crocetti – lcrocetti@ethz.ch

## Slide 6: Data
Zenith Wet Delay (ZWD)
Source: Nevada Geodetic Laboratory (NGL)
  More than 19.000 GPS stations available
Temporal resolution: 5 min  hourly resolution
Spatial resolution: stations distributed globally
Time span: year 2019
Meteorological data
Source: ECMWF ERA5
Temporal resolution: hourly
Spatial resolution: 0.25°
Time span: year 2019
Several variables:
  Specific humidity
  Relative humidity
  Temperature
  Surface pressure
  Total precipitation
  Geopotential
  Wind speed
Laura Crocetti – lcrocetti@ethz.ch

## Slide 7: Data
Meteorological data
Source: ECMWF ERA5
Temporal resolution: hourly
Spatial resolution: 0.25°
Time span: year 2019
Several variables:
  Specific humidity
  Relative humidity
  Temperature
  Surface pressure
  Total precipitation
  Geopotential
  Wind speed
Zenith Wet Delay (ZWD)
Source: Nevada Geodetic Laboratory (NGL)
  More than 19.000 GPS stations available
Temporal resolution: 5 min  hourly resolution
Spatial resolution: stations distributed globally
Time span: year 2019
TARGET
FEATURES
Laura Crocetti – lcrocetti@ethz.ch
  Latitude
  Longitude
  Height
  Time

## Slide 8: Data
Zenith Wet Delay (ZWD)
Source: Nevada Geodetic Laboratory (NGL)
  More than 19.000 GPS stations available
Temporal resolution: 5 min  hourly resolution
Spatial resolution: stations distributed globally
Time span: year 2019
Meteorological data
Source: ECMWF ERA5
Temporal resolution: hourly
Spatial resolution: 0.25°
Time span: year 2019
Several variables:
  Specific humidity
  Relative humidity
  Temperature
  Surface pressure
  Total precipitation
  Geopotential
  Wind speed
TARGET
Aim: predict ZWD in space (and time) using ML algorithms
Laura Crocetti – lcrocetti@ethz.ch
FEATURES
  Latitude
  Longitude
  Height
  Time

## Slide 9: Set up
ML ALGORITHM
standardize features
hyperparameter optimization
cross-validation
train model
EVALUATION
Make ZWD predictions for testing data (y_test_pred)
calculate performance metrics
  RMSE
  R2
TRAINING DATA - 80%
ZWD (y_train)
features (X_train)
TESTING DATA - 20%
ZWD (y_test)
features (X_test)
output: ML model
DATA
ML algorithm: XGBoost, Random Forest
Distribution of training and test stations for all available stations (2019)
Global model for year 2019
Laura Crocetti – lcrocetti@ethz.ch

## Slide 10: Performance of individual test stations
Laura Crocetti – lcrocetti@ethz.ch

## Slide 11: Performance of individual test stations
mean = 12.47 mm
Laura Crocetti – lcrocetti@ethz.ch

## Slide 12: ZWD predictions for 2019
Laura Crocetti – lcrocetti@ethz.ch

## Slide 13: Summary
Global ML-based ZWD model based on meteorological data
Can make predictions of ZWD for every point on Earth (assuming meteorological data is available)
Achieves an average RMSE of 12.47 mm
ML algorithms: XGBoost and Random Forest
atmosphere
Laura Crocetti – lcrocetti@ethz.ch

## Slide 14
Laura Crocetti lcrocetti@ethz.ch
ETH Zurich
Space Geodesy Group
Institute of Geodesy and Photogrammetry
Zurich, Switzerland
www.space.igp.ethz.ch