## Slide 1: Modeling wildfire dynamics and future projections under climate change scenarios: the FLAM approach
Andrey Krasovskiy1, Shelby Corning1, Esther Boere1, Nikolay Khabarov1, Reinis Cimdins2, Florian Kraxner1
EGU General Assembly 2023
Session NH7.2: “The effect of weather and climate extremes on wildfires and their impacts”
April 25, 2023
Vienna, Austria
1) International Institute for Applied Systems Analysis (IIASA), Laxenburg, Austria 2) University of Eastern Finland, Joensuu, Finland

## Slide 2
Mechanistic fire model that uses algorithms to parameterize the impacts of climate, fuel availability, and human activities on wildfire probabilities, frequencies, and burned areas
Operates with a daily time step at various resolutions (100m to 25km)
FLAM was calibrated and validated using the most recent publicly available GIS and remote sensing datasets
Allows for inclusion of additional fire-related factors into model
Ability to model and compare situations locally, regionally, and globally, under different warming and RCP scenarios.
Find more info at: www.iiasa.ac.at/flam
wildFire cLimate impacts and Adaptation Model (FLAM)

## Slide 3: Wildfire climate impacts and adaptation model (FLAM)
Schematic of FLAM workflow
www.iiasa.ac.at/flam

## Slide 4: FLAM calibration approach: Europe
Annual burned areas (in thousands of hectares):
GFED, Global Fire Emissions Database; EFFIS, European Forest Fire Information System.

## Slide 5: FLAM projections for Europe
Chart: Europe
| 1965 | 2005 | 2030 | 2050 | 2090
FLAM_CNRM | 723302.1511 | 963431.4561 | 1288603.3276 | 1623196.6738 | 3795144.159
FLAM_SCIRO | 723279.4317 | 963431.4561 | 1131070.5397 | 1275467.9974 | 2672684.8269
FLAM_MRI | 723372.9512 | 963431.4561 | 918217.0178 | 1230570.8985 | 2235123.2159
PB FLAM_CNRM | 223948.7146 | 317016.2295 | 452078.3607 | 581030.8745 | 1497900.3292
PB FLAM_SCIRO | 223948.7146 | 317016.2295 | 379944.1275 | 428039.2453 | 977026.118
PB FLAM_MRI | 223948.7146 | 317016.2295 | 295008.1481 | 417911.0269 | 784187.2667

## Slide 6: FLAM - captures spatial hot spots in Indonesia
Spatial suppression efficiency (at 25 km2 resolution) calibrated in FLAM using burned area reported in GFED for wildfire in Indonesia, accumulated over 2000-2009
Notes: We see that suppression efficiency is found low in the peatland areas. This parameter is connected to the duration of fire. In some peatland areas fire can last for months, once it is ignited. So far it is rather aggregated indicator, but we will identify what is behind this parameter (infrastructure, land use, etc.)

## Slide 7: FLAM - captures temporal dynamics
Annual dynamics of burned area (wildfire) in Indonesia [MHa]. During the calibration period GFED burned area (black line), accumulated over 2000-2009, is used for FLAM calibration. In 2010-2016 GFED data is used for validation of the burned area estimated by FLAM (red line). GFED uncertainty (grey area).
Source: Krasovskii et al, Modeling Burned Areas in Indonesia: The FLAM Approach. Forests 2018, 9, 437. https://doi.org/10.3390/f9070437
Notes: One can see that red line FLAM projection is close to the black line - data from GFED.
In the validation period we did not use any real (satelite) data

## Slide 8: FLAM - captures seasonal dynamics
Monthly dynamics of burned area (wildfire) in Indonesia [MHa]. (FLAM: red line, data: black line)
See recurring fire season in Indonesia picking each September.
Notes: We could also capture monthly dynamics (FLAM - red line, data - Black)
The fire season is usually in September in Indonesia

## Slide 9: FLAM projection under CC scenarios
Future burned areas projected by FLAM under four RCP scenarios in Indonesia (daily weather from ISIMIP2b). Dashed lines: annual burned areas in Indonesia; solid lines: polynomial trends of second order. Period 2000-2016 is used for calibration, and 2017-2099 for projection. Source: RECEIPT project deliverable.

## Slide 10: Global projections – burned area under RCPs
Calibration period: 2001-2016
Projection period: 2017-2099
Climate data: HadGEM2-ES model (ISIMIP2b)
Forest growth: G4M
Chart: Area burned in forests, mln. ha
Source: IIASA-FLAM, Krasovskiy et al, 2019
FLAM

## Slide 11: FLAM: Globale Waldbrandfläche / Hot Spots (2080-2100) RCP 8.5 Szenario
Source: IIASA-FLAM, Krasovskiy et al, 2019

## Slide 12
Regional Variability and Driving Forces behind Forest Fires in Sweden
Understand vulnerability of Swedish forests to wildfires
1km x 1km spatial grid on a monthly time step, with 6 biogeographical zones
Addition of road density, topography, and campsites to the parameters
Random forest to determine importance features for wildfire probability within zones
Hotspot mapping with visualization in Google Earth Engine (GEE)
Cimdins, R., Krasovskiy, A., Kraxner, F. "Regional Variability and Driving Forces behind Forest Fires in Sweden." Remote Sensing, vol. 14, no. 22, 2022.

## Slide 13
Thank you for your attention!
Contact:
Dr. Andrey Krasovskiy
Research Scholar
Agriculture Forestry and Ecosystem Services (AFE)
Biodiversity and Natural Resources (BNR)
International Institute for Applied Systems Analysis (IIASA)
https://iiasa.ac.at/staff/andrey-krasovskiy
https://iiasa.ac.at/flam

## Slide 14: IIASA Integrated Assessment Framework
air pollution emission
coefficients & abatement costs
Population
Economy
G4M
spatially explicit forest management model
GLOBIOM
integrated agricultural, bioenergy and forestry model
MESSAGE
systems engineering model (all energy sectors, all GHGs, pollutants and water)
socio-economic drivers
carbon and biomass price
agricultural and forest bioenergy potentials,
land-use emissions and mitigation potential
National level Projections
MAGICC
simple climate model
GAINS
GHG and air pollution mitigation model
GHG emissions
demand
response
iteration
MACRO
Aggregated macro-economic model
energy
service
prices
socio-
economic
drivers
EPIC
agricultural crop model
Access
Fuel choice model for cooking
Transport Module Modal split,
cost and value of time
BeWhere
Spatially explicit Techno-economic energy system optimization model
GEO-WIKI.ORG
Citizen Science
FLAM
wildfire climate impacts and adaptation model
Source: IIASA, 2018

## Slide 15
Recent FLAM-related publications - 2
Optimization of the IIASA’s FLAM model to represent forest fires in South Korea1
Optimize FLAM to reflect (seasonal) fire frequency patterns in South Korea
1km x 1km spatial grid on a daily time step
Addition of peatland burning and proximity of forests to agricultural fields to parameters
Alterations to lightning occurrence (daily vs monthly), population density threshold value for ignition, and use of remote sensing moisture data for FFMC
Showed benefits of optimization of FLAM to regional characteristics (spatial patterns, frequency, additional human-related activities)
FLAM workflow diagram
Jo, H.-W., Krasovskiy, A. , Hong, M., Corning, S., Kim, W., Kraxner, F., & Lee, W.-K. (2023). Modeling Historical and Future Forest Fires in South Korea: The FLAM Optimization Approach. Remote Sensing 15 (5) e1446. 10.3390/rs15051446.