## Slide 1: HFC mitigation pathways compatible with 1.5 oC in the context of the Kigali Amendment
Pallav Purohit, Lena Höglund-Isaksson and Zbigniew Klimont
IIASA - Energy, Climate and Environment (ECE) Program
Pollution Management (PM) Research Group
Ninth International Symposium on Non-CO2 Greenhouse Gases (NCGG9)
Amsterdam, The Netherlands
June 21-23, 2023

## Slide 2: The GAINS Model (Greenhouse gas - Air Pollution INteractions and Synergies)
National emission ceilings
Decision making on F-gas management and co-benefit assessment
Emission factor
Emission control options
(F-gas regulations, policies and measures)
Emissions
Costs
Radiative forcing impacts of F-gases (via GWP)
F-gas (HFC, PFC, SF6, NF3) activities
Exogenous projections
Global (i.e., IEA-WEO/MESSAGE)
Regional (i.e., PRIMES/AIM)
National (i.e., MARKAL)
Source: IIASA/GAINS
Macro-economic drivers
Marginal abatement cost-curves for F-gases
Unit costs
Mitigation strategies

## Slide 3: The Kigali Amendment
The Parties to the Montreal Protocol reached agreement at their 28th Meeting of the Parties on 15 Oct 2016 in Kigali, Rwanda to phase-down HFCs.
Countries agreed to add HFCs to the list of controlled substances, and approved a timeline for their gradual reduction by 80-85% by the late 2040s
Entry into force: 1st Jan 2019
Ratification status: 150
  Article 5, Group 2: Bahrain, India, Iran, Iraq, Kuwait, Oman, Pakistan, Qatar, Saudi Arabia, and the United Arab Emirates.
  Non-Article 5, later start: Russia, Belarus, Kazakhstan, Tajikistan, Uzbekistan

## Slide 4: HFC emissions in the baseline, Kigali Amendment (KA) and Maximum Technically Feasible Reductions (MTFR) scenarios
Source: Purohit et al. (2020) Atmos. Chem. Phys., 20: 11305–11327
4.0-5.3 Gt CO2eq
(Velders et al., 2015)

## Slide 5: HFC emissions in the baseline, Kigali Amendment (KA) and Maximum Technically Feasible Reductions (MTFR) scenarios
The 1.5°C-consistent scenarios used in IPCC’s Special Report on Global Warming of 1.5 °C (SR15) include a 75-80% reduction in HFC emissions by 2050, compared to 2010 levels, along with deep and simultaneous reductions of CO2 and all non-CO2 climate-forcing emissions.
Full compliance with the Kigali amendment is expected to achieve a 56% reduction in HFC emissions by 2050, compared to 2010 levels.
56%
75-80%
Source: Purohit et al. (2020) Atmos. Chem. Phys., 20: 11305–11327
4.0-5.3 Gt CO2eq
(Velders et al., 2015)

## Slide 6: Kigali Amendment: A5 Group 1&2 alignment scenario
Chart: a) A5-Groups1&2-alignment scenario
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Non-A5, earlier start | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.2 | 0.2 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15
Non-Article 5, earlier start
Non-Article 5, later start
Article 5, Group 1
Article 5, Group 2

## Slide 7: Kigali Amendment: 95% scenario
Chart: b) 95% scenario
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Non-A5, earlier start | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.2 | 0.2 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15
Non-Article 5, earlier start
Non-Article 5, later start
Article 5, Group 1
Article 5, Group 2

## Slide 8: Kigali Amendment: Combined scenario
Chart: c) Combined scenario
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Non-A5, earlier start | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.2 | 0.2 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15 | 0.15
Non-Article 5, earlier start
Non-Article 5, later start
Article 5, Group 1
Article 5, Group 2

## Slide 9
Source: Salawitch et al. (2018)

## Slide 10: Kigali Amendment : Accelerated combined scenario
Source: Purohit et al. (2022) Nat. Clim. Chang. 12: 339–342

## Slide 11: HFC emissions in the baseline and alternative scenarios
Source: Purohit et al. (2022) Nat. Clim. Chang. 12: 339–342

## Slide 12: HFC emissions in the baseline and alternative scenarios
Source: Purohit et al. (2022) Nat. Clim. Chang. 12: 339–342

## Slide 13: Summary
Hydrofluorocarbon emissions have increased rapidly and are managed by the Kigali Amendment to the Montreal Protocol.
The current ambition of the Kigali Amendment is not consistent with the 1.5 °C Paris Agreement goal.
The start-and-strengthen approach of the Montreal Protocol on refrigerant management shows that accelerated HFC phase-down under the Kigali Amendment could result in additional reductions of 72% in 2050, increasing chances of staying below 1.5 °C throughout this century.

## Slide 14: Thank you! E-mail: purohit@iiasa.ac.at